## Slide 1: Combinational Logic
Word Problem
Write Logic Expression
Boolean Simplification
AOI Logic
Implementation
Create Truth-Table
NO
Simplification
Design Process
Version #1

## Slide 2: Design Specifications to Truth Table
Identify the number of input variables.
Assign variable names and establish the assignment condition for each variable (i.e., What does a 0 or 1 mean for that input?).
Create a truth table.
Example
  A large fuel tank has sensors that monitor temperature and pressure. Both sensors output a logic LOW if they are within safety range. An alarm will sound if either sensor indicates an unsafe condition is present. Create a truth table for this logic design.

## Slide 3: Design Specifications to Truth Table
Identify the number of input variables.
Assign variable names and establish the assignment condition for each variable (i.e., What does a 0 or 1 mean for that input?).
Create a truth table.
Example
  A large fuel tank has sensors that monitor temperature and pressure. Both sensors output a logic LOW if they are within safety range. An alarm will sound if either sensor indicates an unsafe condition is present. Create a truth table for this logic design.
P | T | A
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Assignments :
  P: Pressure Sensor → 0=Safe / 1=Unsafe
  T: Temperature Sensor → 0=Safe / 1=Unsafe
  A: Alarm → 0=Alarm Off / 1=Alarm On

## Slide 4: Example #3: Design Specifications to Truth Table
Example
  Your teacher keeps her final exams in her office. For security reasons, she would like you to design an alarm system for her office. The office has a window and door that are equipped with sensors that output a one when they are secured (i.e., closed). When the alarm system is turned on with a key, the siren should sound if either the window or door is unsecured (i.e., opened).
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next slide.

## Slide 5: Example #3: Design Specifications to Truth Table
Example
  Your teacher keeps her final exams in her office. For security reasons, she would like you to design an alarm system for her office. The office has a window and door that are equipped with sensors that output a one when they are secured (i.e., closed). When the alarm system is turned on with a key, a siren should sound if either the window or door is unsecured (i.e., opened).
K | D | W | S
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Assignments :
  K : Key → 0=System Off / 1=System On
  D : Door Sensor → 0=Open / 1=Closed
  W : Window Sensor → 0=Open / 1=Closed
  S : Siren → 1=On / 0=Off
Solution
Notes: The solution for example #3 is included on this slide. If you print handouts, do not print this page.

## Slide 6: Truth Table to Logic Expression
Example
  Write the logic expression for the output F5 in the truth table below.
X | Y | Z | F5
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 7: Logic Expression to Truth Table
F = X′Y′Z′ + X′YZ + XY′Z + XYZ
Example
  Create the truth table for the following logic expression.
X | Y | Z | F7
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 8: Truth Table to Logic Expression
Example
  Write the logic expression for the output F6 in the truth table below.
A | B | C | D | F6
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 9: Truth Table to Logic Expression
Example
  Write the logic expression for the output F6 in the truth table below.
A | B | C | D | F6
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Solution
Notes: The solution for example #1 is included on this slide. If you print handouts, do not print this page.